## Slide 1
Manitoba Drought Management Strategy
Prepared by:
Abul Kashem, P. Eng.
Surface Water Management Section
Manitoba Conservation and Water Stewardship
PPWB Hydrology Workshop Winnipeg, January 29-30, 2013

## Slide 2: Outline
Context
Defining Drought
Determining Drought
Drought Indicator
Preparedness
Assessment of Drought Stages
Reporting
2

## Slide 3
Historical Drought
Red River 1936
Are we prepared for a prolonged drought?
Are our water supplies sufficient?
How do we know if we are in a drought?
Red River 1988
Winnipeg Free Press, Jan 25, 2012
Aug 2011, near Winnipeg, The Globe and Mail
March 2012
Palliser Triangle
3

## Slide 4
Red River’s low flows
Chart: Red River at Emerson
| Jul | Aug | Sep | Oct | Nov | Dec
1936 | 120.4242 | 79.1056 | 66.7454 | 28.6405 | 23.7317 | 33.4433
1988 | 462.6265 | 281.8137 | 332.3141 | 337.2582 | 309.7125 | 256.74
2012 | 2321.841 | 1730.5102 | 862.1481 | 965.6741 | 1130.9545 | 844.7494
Chart: Red River at Emerson
| Jul | Aug | Sep | Oct | Nov | Dec
1936 | 120.4242 | 79.1056 | 66.7454 | 28.6405 | 23.7317 | 33.4433
1988 | 462.6265 | 281.8137 | 332.3141 | 337.2582 | 309.7125 | 256.74
2012 | 2321.841 | 1730.5102 | 862.1481 | 965.6741 | 1130.9545 | 844.7494
4

## Slide 5
Drought is a natural hazard caused by a shortage of water resulting in direct impacts on both human and environmental wellbeing, for a given period of time, for any location(s) where natural or managed water systems fail to meet the typical water demand for human and environmental uses
Defining Drought
5

## Slide 6
  How do we know if we are experiencing a drought?
  Assess two components:
    Indicators
    Preparedness levels
Determining Drought
6

## Slide 7
  Drought indicators help to determine if the basin conditions are:
    Normal
    Moderately dry
    Severely dry
    Extremely dry
  Developed primary and secondary indicators for Manitoba
    Primary: Precipitation and Streamflow
    Secondary: Groundwater
Drought Indicators
7

## Slide 8
  Precipitation Indicators
  Percent of Median
  Precipitation Percentile
  Streamflow Indicator
  Flow Percentile
  Ground Water Indicator
    Ground Water Level Percentile
Drought Indicators (Contd..)
8

## Slide 9
 | Indicator Thresholds |  |  | 
 | Percent (%) of Median Precipitation | Precipitation Percentile (Lowest 5th-20th-35th ) | Flow Percentile (Seasonal) (Lowest 10th-20th-35th ) | Ground Water Level Percentile (Lowest 0.10th-5th-25th )
 | Actual precipitation compared to % of median for 1, 3 or 12 months | Most current month precipitation compared to historical lowest percentiles | Most current month streamflow compared to historical lowest percentiles for each season | Most current month streamflow compared to historical lowest percentiles for each season
Normal condition | >80% of median for 3 months | >35th | >35th | >25th
Moderately dry | 60%-80% of median for 3 months or 12 months | 20 -35th | 20 -35th | 5 -25th
Severely dry | 40%-60% of median for 1 month or 3 months | 5 -20th | 10 -20th | 10 -20th
Extremely dry | <40% of median for either 1 month or 3 months | = or <5th | = or <10th | = or <10th
Drought Indicators (Contd..)
9

## Slide 10
Chart: Historical Drought (1938-2007), Winnipeg Indicator: % of Median (3 Month) Precipitation
Moderate- 14%, Severe-6%, and Extreme -1% of time
Chart: Historical Drought (1938 -2007), Winnipeg Indicator: Lower 5-20-35th Percentiles of Monthly Precipitation
Moderate- 5%, Severe-6%, and Extreme-1% of time
Drought Indicators (Contd..)
10

## Slide 11
Chart: Historical Drought (1912-2007) Indicator: Lower 10-20-35th Percentiles of Monthly Flow, Seasonal Red River at Emerson
Moderate- 10%, Severe-7%, and Extreme -6% of time
Chart: Historical Drought(1966-2009) Indicator: Lower 0.1-5-25th Percentiles of Monthly Ground Water Levels Sandilands (G05OE001)
| 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
Moderate | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 12 | 5 | 0 | 9 | 7 | 0 | 1 | 12 | 12 | 12 | 12 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Severe | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 12 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Extreme | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Moderate- 10%, Severe-7%, and Severe -6% of time
Drought Indicators (Contd..)
11

## Slide 12
  Assessment of drought stage also requires information on basin’s preparedness level
  Preparedness is the basin’s resiliency to withstand a drought
  Need to assess preparedness across basins – water supply infrastructure, communication, etc.
Preparedness
12

## Slide 13
  Drought stages (Normal, Moderate, Severe and Extreme) determined through assessment of drought indicators and preparedness level
Assessment of Drought Stage
Drought Indicator | Preparedness Level |  |  | 
 | None | Low | Medium | High
Normal | Normal | Normal | Normal | Normal
Moderately dry | Moderate | Moderate | Moderate | Normal
Severely dry | Severe | Severe | Severe | Moderate
Extremely dry | Extreme | Extreme | Severe | Moderate
13

## Slide 14
http://www.gov.mb.ca/conservation/waterstewardship/water_info/hydrology/drought.html
Reporting
Reporting on Water Availability and Drought Conditions
14

## Slide 15
  Thank you
15